## Slide 1: Mobility Models for UAV Group Reconnaissance Applications
By Paziewski Hayley, Etcheverry Jérémy, Tessier Alexis, Testa Mickaël, Castagnet Florian
26/11/2013
Master 2 Computer Science
Study and Research Project
2013-2014
University of Bordeaux 1 - Science and Technology
Responsible of Directed Works :
CHAUMETTE Serge and AUTEFAGE Vincent
Desbarats Pascal
Responsible of TD:

## Slide 2
Problematic
  Use mobility model that most closely matches the results of real-world scenario.

## Slide 3
Introduction
MANET
  Mobile Ad Hoc Network
  Networks of mobile entities
  Collect, process and transmit data
UAV
  Application of mobility models with UAVs
2 differents mobility models
  Random Waypoint
  Distributed Pheromone Repel

## Slide 4
Scenarios
Objectives
  Scan area in a limited time
  Scan the entire area regularly, but at least once every hour
Characteristics
  Square with a side length of 30 Km
  10 UAVs per run
  Fixed wing aircraft
  UAVs start at the middle of south edge

## Slide 5
Scenarios
Requirements
  UAVs are autonomous
  Regularly scans
  Randomness element in mobility models
  Data must be returned to the C&C
  Lost or unaivalable UAVs is not important
  Communication bandwidth is limited

## Slide 6
Models
Properties
  Min an Max air speed and can’t changed direction in an instant
  No collisions thanks to altitude adjustements
  Flight altitude: 3500 meters (11 000 feet)
  Flight speed: 150 km/h (41.7 m/s, 81.0 knots)
  Turn radius: 500 meters
  Infinite bandwidth between 2 UAV’s within 8000m
  Scan zone 2000x1000 m

## Slide 7
Models
Random Mobility Model

## Slide 8
Models
Pheromone models
  One pheromone map per UAV
  Marks the areas when they have been scanned
  Broadcast regularly a local area pheromone map

## Slide 9
Models
Pheromone models

## Slide 10
Evaluations
Scan coverage
Scan charateristic
Communication

## Slide 11
Evaluations
Scan Coverage
Theory : 900km² in 18 min
Prevision : 40 min because of several turnings
Rapidity of scanning : 0,083 km²/s per UAV

## Slide 12
Evaluations
Scan characteristic
Both models manage quite well to avoid rescanning a recently scanned area
Pheromone > Random

## Slide 13
Evaluations
Communication
Low constant connectivity
  More UAVs for a fully network connected

## Slide 14
Conclusion
Good model for scan coverage and reconnaissance scenario …
… But coverage and connectivity of communications are two conflicting objectives.
Possiblity amelioration is to temporary storage data and relax the limited bandwidth.

## Slide 15: Do you have any questions ?

## Slide 16
Notes: Voici un autre exemple de diapositive de vue d’ensemble.

## Slide 17: Nouveau travail
Notes: Utiliser un en-tête de section pour chacun des sujets afin de définir une transition claire pour l’audience.

## Slide 18
Notes: Ajoutez des diapositives à chaque section de sujet, y compris des diapositives contenant des tableaux, des graphiques et des images.
Voir exemple dans la section suivante de tableau, de graphique, d’image et de vidéo.

## Slide 19: Ressources
<Texte du site intranet ici> <lien hypertexte ici>
<Texte de support de lecture supplémentaire ici> <lien hypertexte ici>
Cet ensemble de diapositives et ressources connexes : <lien hypertexte ici>

## Slide 20: Annexe
Notes: Votre présentation est-elle aussi claire que possible ? Pensez à placer du contenu supplémentaire dans l’annexe.
Utilisez des diapositives en annexe pour y placer du contenu auquel vous pouvez faire référence pendant la diapositive relative aux questions ou que les participants peuvent approfondir ultérieurement.