## Slide 1: Mobility Models for UAV Group Reconnaissance Applications
By Castagnet Florian, Etcheverry Jérémy, Paziewski Hayley, Tessier Alexis,Testa Mickaël
Master 2 Computer Science, Network, System and Mobility
Study and Research Project on paper
2013-2014
Directors of tutorial classes :
AUTEFAGE Vincent and CHAUMETTE Serge
Erik Kuiper & Simin Nadjm-Tehrani
ICWM 2006
22/01/2014

## Slide 2
Outline
Context
Problematics
Study of existing models
Our article studied
Models of our study
Experiments
Comparison of 2 models
Our Implementation
Conclusion

## Slide 3
Context
  UAV
  Swarm of UAVs
  Mobility models
   How do they move ?
Figure 1. Source : http://rain.aa.washington.edu"

## Slide 4
Problematics
How to scan an area properly ?
As much and as quickly possible, in a limited time and at least,
once every hour.
Figure 2 . Source : "http://www.swiss-uav.com "
Figure 3. Source : " http://technorati.com "

## Slide 5
Study of existing models
Existing Models
Random Walk
Random WayPoint
[1] : Result pattern of Random Walk
[2] : Result pattern of Random Waypoint

## Slide 6
Study of existing models
City Section
Distributed Pheromone
Blue : repulsive
Green : attractive
[3] : Street scenario corresponding to a square area size 1900x1900
[4] : Attractive and Repulsive Pheromones For Surveillance

## Slide 7
Our article studied
Introduction
MANET
  Mobile Ad Hoc Network
  Networks of mobile entities
  Collect, process and transmit data
UAV
  Application of mobility models with UAVs
2 different mobility models
  Random Waypoint
  Distributed Pheromone Repel

## Slide 8
Models of our study
  Random Waypoint model
  Each drone is independent
  No backup position
  Random target

## Slide 9
Models of our study
From : “Mobility Models for UAV Group Reconnaissance Applications”
By : E. Kuiper and S. Nadjm-Tehrani.
  Random Waypoint model

## Slide 10
Models of our study
  Distributed Pheromone Repel model
  Coordination of UAVs thanks to pheromones
  Adaptative
  UAV
[2] : Result pattern of Random Waypoint

## Slide 11
Models of our study
  Distributed Pheromone Repel model
One pheromone map per UAV
Marks the areas when they have been scanned
Regularly broadcast a local area pheromone map (when a distance is inferior to 8 km between two UAVs)

## Slide 12
Models of our study
From : “Mobility Models for UAV Group Reconnaissance Applications”
By : E. Kuiper and S. Nadjm-Tehrani.
  Distributed Pheromone Repel model

## Slide 13
Experiments
Scenarios for the 2 models
Characteristics
  Square with a side length of 30 Km
  10 UAVs per run
  Fixed wing aircraft
Requirements
    Data must be returned to the C&C
    No excessive use of bandwidth
    (no quantification in the article)
1
1 : Command and Controler center

## Slide 14
Experiments
  Expected results :
  Scan the area in 40 min
Mobilities Models | RandomWalk | Pheromone
Time to scan the area | 80% of the area in 120 min | 90% of the area in 50 min
Connectivity | Low | Low
Obtained results :

## Slide 15
Experiments
  Our point of view about limitations
  Speed and shift (direction)
  Coverage and connectivity of communications are two conflicting objectives.
  Comparison between pheromone and random model not adapted
  Communication between UAVs are unrealistic

## Slide 16
Comparison of 2 models
Scan characteristic
Both models manage quite well to avoid rescanning a recently scanned area.
From : “Mobility Models for UAV Group Reconnaissance Applications”
By : E. Kuiper and S. Nadjm-Tehrani.

## Slide 17
Our Implementation
Everything was done
10 nodes/models
Margin calculation
Percentage of scan
Tracking display
All models
Pheromone model
Presence of C&C does not move
Communication

## Slide 18
Our Implementation
JBotSim
Pheromone model

## Slide 19
Our Implementation
JBotSim
Random Walk model

## Slide 20
Our Implementation
JBotSim
Random Waypoint model

## Slide 21
Our Implementation
Interpretation of results
At the beginning, the Random models are more efficients
At the end, random models are stable
Pheromone model is more effective than the others models to reach 100% of scan.

## Slide 22
Our Implementation
Comparison with article
Chart: Scan coverage
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 17 | 19 | 20 | 21 | 22
Walk | 14 | 24.7 | 34 | 44 | 50 | 57 | 62.5 | 68.4 | 72.5 | 75.9 | 78.4 | 80.3 | 82.6 | 85.6 | 88.1 | 90 | 91 | 93 | 95 | 96.3
Waypoint | 21 | 36 | 47 | 55 | 62 | 66 | 70 | 73 | 76 | 78 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 89 | 90
Pheromone | 10.75 | 20 | 25.4 | 30.8 | 38 | 51.5 | 68.5 | 71.4 | 73 | 80 | 81.2 | 82 | 84 | 84.8 | 86.4 | 88.3 | 90 | 95 | 96.6 | 98

## Slide 23
Mobility Model Scenarios | Semi-Random-Circular-Movement | Distributed Pheromone Repel | Smooth turn
Scan Coverage | X | X | 
Airborne Networks |  |  | X
Importance of the Mobility Model choosen
Our Implementation

## Slide 24
Conclusion
Good model for scan coverage and reconnaissance scenario.
Characteristics of evaluation and experiments are unrealistic
Possible improvement is to store and forward data and relax the limited bandwidth.
Figure 5. Source : " http://www.vikingaero.com "
Figure 4. Source : " http://fr.depositphotos.com "

## Slide 25: Do you have any questions ?
Figure 6. Source : " http://titanaerospace.com "

## Slide 26: References
E. Kuiper and S. Nadjm-Tehrani.
Mobility models for uav group reconnaissance applications. In Wireless and Mobile Communications, 2006. ICWMC ’06. International Conference on, page 33, July 2006.
"http://dept-info.labri.fr/~desbarat/PER/sujets/Autefage1-article.pdf "
[1] && [2] : A. Jardosh, E. M. Belding-Royer, K. C. Almeroth, S. Suri. Towards Realistic Mobility Models for Mobile Ad Hoc Networks. 9th annual International Conference on Mobile Computing and Networking. September 2003. ACM Press
[3] A. K. Saha, D. B. Johnson. Modeling Mobility for Vehicular Ad Hoc Networks. First ACM Workshop on
Vehicular Ad Hoc Networks. October 2004. ACM Press
[4] J. A. Sauter, R. Matthews, H. V. D. Parunak, S. A.Brueckner. Performance of Digital Pheromones for Swarming Vehicle Control. Fourth International Joint Conference on Autonomous Agents and Multi-Agent
Systems. July, 2005. ACM Press