## Slide 1: Mobility Models for UAV Group Reconnaissance Applications
By Paziewski Hayley, Etcheverry Jérémy, Tessier Alexis, Testa Mickaël, Castagnet Florian
22/01/2014
Master 2 Computer Science
Study and Research Project
2013-2014
University of Bordeaux 1 - Science and Technology
Responsible of Directed Works :
CHAUMETTE Serge and AUTEFAGE Vincent
Erik Kuiper & Simin Nadjm-Tehrani
IEEE lecture 2006

## Slide 2
Plan
Context
Problematic
Study of existing
Our article
Models of our study
Experiments
Comparison of 2 models
Our Implementation
Conclusion

## Slide 3
Context
  UAV
  Swarm of UAVs
  Mobility models
   How do they move ?

## Slide 4
Problematic
How well scan an area ?
As much and as quickly possible, in a limited time and at least,
once every hour.
Figure 1 . Source : "http://www.swiss-uav.com "
Figure 2. Source : " http://technorati.com "

## Slide 5
Study of existing
Existing Models
Random Walk
Random WayPoint
[1] : Result pattern of Random Walk
[2] : Result pattern of Random Walk

## Slide 6
Study of existing
City Section
Distributed Pheromone Repel
Blue : repulsive
Green : attractive
[3] :
[4] : Attractive and Repulsive Pheromones For Surveillance

## Slide 7
Our Article
Introduction
MANET
  Mobile Ad Hoc Network
  Networks of mobile entities
  Collect, process and transmit data
UAV
  Application of mobility models with UAVs
2 differents mobilities models
  Random Waypoint
  Distributed Pheromone Repel

## Slide 8
Models of our study
  Random Waypoint model
  Each drones are independant
  No backup position
  Random target

## Slide 9
Models of our study
From : “Mobility Models for UAV Group Reconnaissance Applications”
By : E. Kuiper and S. Nadjm-Tehrani.
  Random Waypoint model

## Slide 10
Models of our study
  Distributed Pheromone Repel model
  Coordination of UAVs thanks to pheromones
  Dynamic UAV

## Slide 11
Models of our study
  Distributed Pheromone Repel model
One pheromone map per UAV
Marks the areas when they have been scanned
Broadcast regularly a local area pheromone map (when a distance is inferior to 8 km)

## Slide 12
Models of our study
From : “Mobility Models for UAV Group Reconnaissance Applications”
By : E. Kuiper and S. Nadjm-Tehrani.
  Distributed Pheromone Repel model

## Slide 13
Experiments
Scenarios for the 2 models
Characteristics
  Square with a side length of 30 Km
  10 UAVs per run
  Fixed wing aircraft
Requirements
    Data must be returned to the C&C
    No excessive use of bandwidth
    (communication of 1 message/s/UAV)

## Slide 14
Experiments
  Expected results :
  Scan the area in 18 min
Mobilities Models | RandomWayPoint | Pheromone
Time to scan the area | 80% of the area in 120 min | 90% of the area in 50 min
Connectivity | Low | Low
Obtained results :

## Slide 15
Experiments
  Limitations
  Speed and shift (direction)
  Coverage and connectivity of communications are two conflicting objectives.
  Absolutely unrealistic !!!!!!

## Slide 16
Comparison of 2 models
Scan characteristic
Both models manage quite well to avoid rescanning a recently scanned area.
From : “Mobility Models for UAV Group Reconnaissance Applications”
By : E. Kuiper and S. Nadjm-Tehrani.

## Slide 17
Our Implementation
Everything was done
10 nodes/models
Margin calculation
Percentage of scan
Tracking display
All models
Pheromone model
Presence of C&C does not move
Communication

## Slide 18
Our Implementation
JBotSim
Pheromone model

## Slide 19
Our Implementation
JBotSim
Random Walk model

## Slide 20
Our Implementation
JBotSim
Random Waypoint model

## Slide 21
Our Implementation
Interpretation of results
At the beginning, Random model more efficiency
Pheromone : sharp increase because of C&C communication
At the end, random models are stable
Pheromone model is more effective that the others models to reach 100% of scan.

## Slide 22
Our Implementation
Comparison with article
Chart: Scan coverage
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 17 | 19 | 20 | 21 | 22
Walk | 14 | 24.7 | 34 | 44 | 50 | 57 | 62.5 | 68.4 | 72.5 | 75.9 | 78.4 | 80.3 | 82.6 | 85.6 | 88.1 | 90 | 91 | 93 | 95 | 96.3
Waypoint | 21 | 36 | 47 | 55 | 62 | 66 | 70 | 73 | 76 | 78 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 89 | 90
Pheromone | 10.75 | 20 | 25.4 | 30.8 | 38 | 51.5 | 68.5 | 71.4 | 73 | 80 | 81.2 | 82 | 84 | 84.8 | 86.4 | 88.3 | 90 | 95 | 96.6 | 98

## Slide 23
Conclusion
Good model for scan coverage and reconnaissance scenario.
Absolutely unrealistic
Possiblity amelioration is to temporary storage data and relax the limited bandwidth.
Figure 3. Source : " http://www.vikingaero.com "
Figure 4. Source : " http://fr.depositphotos.com "

## Slide 24: Do you have any questions ?
Figure 5. Source : " http://titanaerospace.com "
Figure 6.

## Slide 25: Ressources
E. Kuiper and S. Nadjm-Tehrani.
Mobility models for uav group reconnaissance applications. In Wireless and Mobile Communications, 2006. ICWMC ’06. International Conference on, page 33, July 2006.
"http://dept-info.labri.fr/~desbarat/PER/sujets/Autefage1-article.pdf "
[1] && [2] : A. Jardosh, E. M. Belding-Royer, K. C. Almeroth, S. Suri. Towards Realistic Mobility Models for Mobile Ad Hoc Networks. 9th annual International Conference on Mobile Computing and Networking. September 2003. ACM Press
[3] A. K. Saha, D. B. Johnson. Modeling Mobility for Vehicular Ad Hoc Networks. First ACM Workshop on
Vehicular Ad Hoc Networks. October 2004. ACM Press
[4] J. A. Sauter, R. Matthews, H. V. D. Parunak, S. A.Brueckner. Performance of Digital Pheromones for Swarming Vehicle Control. Fourth International Joint Conference on Autonomous Agents and Multi-Agent
Systems. July, 2005. ACM Press